## Slide 1
Dahua
Parking Guidance System Solution

## Slide 2
Requirement

## Slide 3
Requirements
Existing Problem
Hard to find
evidence for accidents
Hard to find an
available parking space
Hard to manage the
parking lot

## Slide 4
Requirements
An Excellent System
Efficient for finding space
Visualized parking management
High definition surveillance
Find evidence for disputes
Reasonable construction cost
A stable
running system

## Slide 5
Requirements
System Overview
LRP
Space Detection
Video Surveillance
Guidance
Authentication
Analytics
智能化实战平台
深化业务实战应用
Front-End
Subject
Manage Center
Parking Guidance
Space Protection
Accurate Charge

## Slide 6
System Design

## Slide 7
Parking Guidance Process
System Design
Guidance
Available
Full
Guidance
Entry

## Slide 8
System Topology
System Design
DSS4004-H
Management Center
E
Entrance & Exit
Parking Area
Guidance Screen
Detector
LPR Camera
Guidance Screen
Barrier
Access Management
Parking Area
Guidance
EVS7024S-R
Controller
I/O
Network cable

## Slide 9
Entrance & Exit
System Design
One platform to manage multiple entrances and exits
Induction Loop
Induction Loop
Induction Loop
Camera
Barrier
Camera
Barrier
Intelligent parking system
Entrance1
Management center
Exit1
Barrier opens and camera snapshots when the first induction loop is triggered
Induction Loop

## Slide 10
Entry Process
System Design
Induction Loop
Induction Loop
Entrance
Plate number recognition A0011X，
Time：16:05
DSS4004-PSM
Data is uploaded
to the platform
Notes: Car reaches the entrance—Trigger the loop—The entrance camera captures an image and recognizes plate number---open the barrier and uploaded the date to the platpform software to track the car

## Slide 11
Exit Process
System Design
Car reaches the exit
trigger the loop
The entrance camera captures an image and recognizes plate number
Camera capture a image and do LRP
The exit camera triggers barrier to open
Data is uploaded to the platform and compare the plate number
Car leaves

## Slide 12
System Design
Exit Process
Plate number recognition A0011X，
Time：19:15
Induction Loop
Induction Loop
Exit
DSS4004-PSM
Plate number check and comparison
Notes: Car reaches the entrance—Trigger the loop—The entrance camera captures an image and recognizes plate number---upload the date to the platpform software to compare the plate number---camera trigger to open the barrier

## Slide 13
Parking Guidance
System Design
Outdoor screen
Position terminal
Switch
Guidance screen
Switch
Guidance screen
Parking Area
Manage center
All the information such as space status, vehicle type and images are uploaded to the platform
Parking detection camera deployed in cascade mode
Each detection camera covers 2 or 3 spaces. More than 20 detection cameras can be cascaded.
  DSS4004-PSM

## Slide 14
Space Detection
System Design
Detection Camera is able to detect the parking status by vehicle type even without plate number
10
9
8
50
49
48

## Slide 15
System Management
Solution Design
Alarm Linkage
Electronic map
Record storage
Function
History Search
24-Hour real-time Surveillance
Image storage
Device management
Visualized space status
Reports
Vehicle Flow Reports
Parking history Reports
Other Reports
Device
LRP Camera
Detection Camera
Barrier

## Slide 16
Management Client
Solution Design
Entrance History
Visualized Parking Lot

## Slide 17
Highlight

## Slide 18
Show Available Parking Space
Guidance screen will show the available parking space number to drivers and guide then to the right direction
Show Accurate Position
Drivers can search available spaces according to the light indicator and guidance screen indication.
Fast Guidance
Highlight

## Slide 19
Record
Snapshot
All-Round Monitoring
Highlight
Cover 3 Parking Spaces

## Slide 20
Simplify Deployment
Highlight
Traditional way
Innovative way
Simplify Deployment & Cost Down
Reduce UTP cable deployment and cost （83%）
Reduce the quantities of switches
Reduce the cost of cable bridge（63% ）
Notes: 按一排10个摄像机，30个车位来计算
双网口网络级联模式：

## Slide 21
Cost Down
Highlight
Two cameras inside make cost down
Traditional way only cover 2~3 parking spaces
Innovative way can cover 6 parking spaces
Reduce the cost of camera（about 50% ）
Traditional way
Innovative way

## Slide 22
Product

## Slide 23
Parking System Platform
Product
DSS4004-PSM
Processor | Baytrail J1900platform, 4core 2.0G CPU
Operating System | Embedded Linux
Memory | 8GB,expansible,ECC validation
Ethernet Interface | 4 * 100/1000Mbs
USB Interface | 2* front USB3.0 2* back USB2.0
VGA Interface | 1
Disk | 4* 2.5’’, full built-in，or 2* 3.5’’
Disk Mode | Single, RAID0, RAID1, RAID5
Power Supply | 100V ~ 240V，47 ~ 63Hz
Consumption | 10W~200W (Disk included)
Temperature | 0℃~50℃
Installation | Standard 19’’ rack-mounted
Second Development | Support SDK

## Slide 24
Central Storage
Product
EVS7024S-R
Controller | Single
Processor | 64 bit high-performance multi-core processor
Memory | 8G standard, up to 16G
Operating System | Embedded Linux
SAS Interface | 2
1000 Mbps Ethernet Port | 1 Mgmt, 4 Data
HDD Compatibility | 1T,2T,3T,4T, support mixed SAS and SATA HDDs, support SSD, 2.5 inch HDD
Power Redundancy | Dual power supply
Cluster Mode | Support N+M cluster
Video Stream Mode | Support RTP/RTCP/RTSP/UDP/HTTP/NTP/SNMP/iSCSI/SMB/NFS/FTP protocols
Streaming Media Protocol | Support access protocol such as ONVIF,PSIA
Performance | Up to 512ch(1024Mbps) front-end access, storage, transmit, 64ch(128Mbps) network playback

## Slide 25
LPR Camera
Product
ITC237-PW1A-IRZ
Resolution | 2 Mega，1920(H)*1080(V)
Image Sensor | 1/1.9 inch 2 Megara CMOS
HD Video Format | H.264 standard, main profile 5.0
HD Image Resolution | 1920(H)*1080(V)
HD Video Resolution | 1920(H)*1080(V)
HD Video Frame Rate | 50fps
2 LED Light build-in, brightness adjustable
Support plate Recognition (license plate and color)
Support two way vehicle snapshot (loop and video)

## Slide 26
Barrier
Product
DH-IPMECD Series
Protocol | RS485
Input voltage | AC220±10%，50Hz
Service life | >3.5 million times
Temperature | -25℃ to 50℃
Speed | Series D: 1.6-2s, Series C:3s Series B:6s
Type | straight/crank arm/lighting rod
Length | 3/ 4/ 6 m
Protection Level | IP44
Perform open and close according to the signal from entrance camera and induction loop or from platform

## Slide 27
Detection Camera
Product
  Embedded with OCR, LPR, detect the parking space, light indication
  Support SDK to integrate with parking management platform
Sensor | 1/3 inch CMOS
Monitor scene | 2/3 parking space
Image resolution | 2048×1536, 2304×1296
Video resolution | 2048×1536, 2304×1296
Day/Night: | Electronic color to black/white
lens | 2.8/3.6mm lens optional
Input Voltage | 8V – 26V
Temperature | -30℃ -- 60℃
Ethernet Interface | 2, 10/100M optional
ITC314-PH1A-F2
ITC314-PH1A-F3

## Slide 28
Detection Camera
Product
  Embedded with OCR, LPR, detect the parking space, light indication
  Support SDK to integrate with parking management platform
Sensor | 1/3 inch CMOS
Monitor scene | 4/6 parking space
Image resolution | 2048×1536, 2304×1296
Video resolution | 2048×1536, 2304×1296
Day/Night: | Electronic color to black/white
lens | 2.8/3.6mm lens optional
Input Voltage | 8V – 26V
Temperature | -30℃ -- 60℃
Ethernet Interface | 2, 10/100M optional
ITC314-PH1A-TF2
ITC314-PH1A-TF3

## Slide 29
Indoor LED Screen
Product
Size | 480*380*102 mm 860*380*102 mm 1240*380*102 mm
Input voltage | AC220V
Distance between pixel | 5 mm
Protocol | RS485
Temperature | -10℃~70℃
DH-IPMPGI-110AA
DH-IPMPGI-120AA
DH-IPMPGI-130AA

## Slide 30
Entrance Controller
Product
Size | 400*296*1504（mm）
Display Panel Size | 305mm×76mm
Input voltage | AC220V
Interface | RS485 * 3, RS232 * 3, 1 loop input, RJ45 100M * 1
Card Writer | Built-in
Temperature | -30℃ to 70℃
Humidity | 20～90％RH
Record entry/exit time
Trigger the barrier to open
DH-IPMECK-200EB
DH-IPMECK-200OB

## Slide 31
Outdoor LED Screen
Product
Number Display Range | 0-999 0-9999 0-99999
Input voltage | AC220V
Display Color | Green
Protocol | RS485
Temperature | -10℃~70℃
DH-IPMPGI-140AA
DH-IPMPGI-150AA
DH-IPMPGI-160AA

## Slide 32
Thank you！
Make your life safe
DAHUA